## Slide 1: PLP Instructions for Project 1
By Christopher Mar

## Slide 2: Register Usage
For this project use only registers in the ranges:
  $t0 through $t9
  $s0 through $s7
  $a0 and $a1
  $v0

## Slide 3: Assembler Directives
.org 0x10000000
  PLP adds this to the top of every new PLP project
  Tells the assembler where, in memory (RAM) to place the instructions that follow it

## Slide 4: Assembler Directives
label:
  Denotes the location of the memory address for the instruction immediately after it
  Target for were to go from a branch or jump instruction

## Slide 5: Pseudo-Operations
li $rd, imm32
  Load immediate
  Loads an immediate value, imm32, into the register, $rd
  For example: li $t0, 321
    Puts the value 321 into the register $t0

## Slide 6: Memory Operations
lw $rt, imm($rs)
  Load word
  2 things are happening
    An address is calculated by adding the immediate value, imm, to the value stored in register $rs
    The value at the memory address that was just calculated is copied into $rt

## Slide 7: Memory Operations
For example, put the value stored at the address 0x10000004 into the register $t1 we would want to use the following:
li $s0, 0x10000004
lw $t1, 0($s0)

## Slide 8: Branch
beq $rt, $rs, my_label
  beq (Branch If Equal)
    If the value in $rt is equal to the value in $rs then the program goes to the label, my_label
    We call this branching
  bne (Branch If Not Equal)
    Branches if the register values are not equal

## Slide 9: Jump
j my_label
  Jump
  When this instruction is reached, the program goes to the label, my_label
  Note that labels in jump and branch instructions don’t have a colon (‘:’) following them

## Slide 10: Branch Delay Slot
Branches and Jumps take 2 instructions to move to the new address
  This means the instruction immediately after one of these instructions is always run
For now, add a nop after any branch of jump instruction

## Slide 11: Arithmetic
addu $rd, $rs, $rt
  Add
  Result is that $rd gets the value of $rs plus $rt

## Slide 12: Arithmetic
For example, if $t0 contains 5 and $t1 contains 10
  addu $t2, $t0, $t1
results in $t2 having the value 15

## Slide 13: Commenting
Anything in a line that follows a number sign (#) is a comment and will be ignored when running
  Syntax highlight color is green

## Slide 14: Memory Mapped I/O
Memory mapped I/O:
  Input and output (I/O) devices use the same address bus as memory (RAM)
    This means that you read the value of an I/O device the same way you would a memory location
  Useful for Project 1: The switches are located at the address 0xf0100000

## Slide 15: Demo of Project 1