## Slide 1: UART
Christopher Mar

## Slide 2: ASCII
Computers only “understand” binary so how are characters stored?
ASCII
  American Standard Code of Information Exchange

## Slide 3: ASCII
Each character is represented by 7-bit value
  Numbers start sequentially at 48 (0x30)
    0 is 0x30
    9 is 0x39
  ‘=’ has the value 61 (0x3D)

## Slide 4: Polling an I/O Device
Project 1 used polling to read the switches
Example uses polling to increment counter while switch is pressed

## Slide 5: UART
Universal Asynchronous Transmitter/Receiver
Used for serial communication
  One bit at a time in each direction
  Other common serial interfaces include:
    SPI
    I2C
    RS-232
    SATA
    USB

## Slide 6: Interface
PLPTool UART
PLP UART
------------------------------00
0xF0000000: Command Register
------------------------------00
0xF0000004: Status Register
------------------------01001000
0xF0000008: Receive Buffer
------------------------01001000
0xF000000C: Send Buffer

## Slide 7: UART Registers
Command Register
  Address: 0xF0000000
  Write only
  Bit 0: Send
    Transmits byte currently in send buffer
  Bit 1: Clear Status
    Puts next byte into receive buffer
    Clears status register ready bit if there are no more characters

## Slide 8: UART Registers
Status Register
  Address: 0xF0000004
  Read only
  Bit 0: CTS (Clear To Send)
    If 1, UART is ready to transmit a byte
  Bit 1: Ready Bit
    If 1, a byte is in the receive buffer that hasn’t been used

## Slide 9: UART Buffers
Receive Buffer
  Address: 0xF0000008
  Contains byte received by UART
Send Buffer
  Address: 0xF000000C
  Location where byte to be transmitted is stored

## Slide 10: Typical Send Procedure
Wait for clear to send bit in status register to be 1
------------------------------10
Clear to Send bit
0xF0000004: Status Register

## Slide 11
Wait for clear to send bit in status register to be 1
Store byte to be sent in send buffer
------------------------01001000
0xF000000C: Send Buffer
Typical Send Procedure

## Slide 12: Typical Send Procedure
Wait for clear to send bit in status register to be 1
Store byte to be sent in send buffer
Write a 1 to the send bit in the command register
0xF0000000: Command Register
------------------------------01
Send bit

## Slide 13: Typical Receive Procedure
Wait for ready bit in status register to be 1
------------------------------10
0xF0000004: Status Register
Ready bit

## Slide 14
Wait for ready bit in status register to be 1
Read byte in receive buffer
0xF0000008: Receive Buffer
------------------------01001000
Typical Receive Procedure

## Slide 15: Typical Receive Procedure
Wait for ready bit in status register to be 1
Read byte in receive buffer
Write a 1 to the clear status bit in the command register
0xF0000000: Command Register
------------------------------10
Clear Status bit

## Slide 16: Bit Masking
How do you access a single bit at a 32-bit register?
Bit masking takes advantage of AND operation
  Only the bits set in your mask are the ones that will be kept

## Slide 17: Bit Masking
Example: Find out if the third bit in a register $t0 set (place answer in $t2)
li $t1, 0b100
  Create a mask
  AND value register with mask
and $t2, $t0, $t1

## Slide 18: Writing to Memory
Store word instruction
  Same format as load word (lw)
  sw $t0, 0($t1)
  $t0 is now the value being written to the calculated memory address

## Slide 19: Memory Access Offset
Address | Contents
0xF0000000 | 0x00000000
0xF0000004 | 0x00000000
0xF0000008 | 0x00000000
0xF000000C | 0x00000000
$s0
li $s0, 0xF0000000

## Slide 20: Memory Access Offset
Address | Contents
0xF0000000 | 0x00000000
0xF0000004 | 0x00000001
0xF0000008 | 0x00000000
0xF000000C | 0x00000000
$s0
li $s0, 0xF0000000
lw $t1, 4($s0) #UART Status Register
$t1
Copied

## Slide 21: PLP Microarchitecture