## Slide 1: Polling vs. Interrupts
Christopher Mar

## Slide 2: Polling
A loop that is exited when a condition is met
  Typically a while loop

## Slide 3
Advantages
Simple to Implement
Easy to debug
  Step through waiting to exit a loop
Disadvantages
Program cannot do anything else while polling
  Busy wait loop
  Not as big of a problem for Project 2 since we have nothing to do until we get all characters
Polling

## Slide 4: Interrupt
Signal to the processor that something needs to be attended to

## Slide 5: Interrupts Terms
Interrupt Service Routine (ISR)
  AKA Interrupt handler
  Section of code that is run when an interrupt occurs
Interrupt Vector ($iv)
  Register that contains the address to jump to

## Slide 6: Interrupts Terms
Interrupt Return Address ($ir)
  Register that contains the address of the instruction following the last executed instruction before the interrupt
  Used to determine where to jump to after the interrupt has been handled by ISR

## Slide 7: Using PLP Interrupts
Interrupt Controller
  Mask (0xf0700000)
    Set bits to enable specific devices to cause interrupts
  Status (0xf0700004)
    Indicates which device(s) triggered an interrupt

## Slide 8: Interrupt Process
Program Instructions
ISR
Interrupt Occurs
$iv
$ir
$ir set to next instruction
Jump to address in $iv
Jump to $ir

## Slide 9
Advantages
Only handles I/O when ready
Disadvantages
Instructions are not executed sequentially
  Unexpected register changes
  An ISR doesn’t know what was happening when it was jumped to
Can be harder to debug
Interrupts

## Slide 10: The Choice is Yours