## Slide 1: Modularity and Functions
Christopher Mar

## Slide 2: Instructions in Memory
.org assembler directive indicates where following instructions are located
Each instruction is assembled directly to a single 32-bit word that is located in RAM
CPU View

## Slide 3: Instructions in Memory

## Slide 4: Load Word (lw)
li $s0, 0x10000000
lw $t0, 4($s0)
Address | Contents
0x10000000 | 0x3C12f010
0x10000004 | 0x36520000
0x10000008 | 0x3C080000
0x1000000C | 0x35080002
$s0
$t0
Copied

## Slide 5: Store Word (sw)
li $t0, 0x250
sw $t0, 8($s0) # $s0 = 0x10000000
Address | Contents
0x10000000 | 0x3C12f010
0x10000004 | 0x36520000
0x10000008 | 0x00000250
0x1000000C | 0x35080002
$s0
$t0
Copied

## Slide 6: Jump-And-Link
jal label
  Performs a jump to label just like j instruction
  Stores address of next instruction in register $ra
    Return address

## Slide 7: Jump Register
jr $rs
  Performs a jump j to the address stored in $rs
  Typically used to return to where jal jumped from

## Slide 8: jal/jr Example

## Slide 9: Stack
In PLP is implemented with:
  Stack pointer ($sp)
  Push pseudo-op
  Pop pseudo-op
Stack grows upwards in memory (address gets smaller) so start at the bottom

## Slide 10: Stack
Initialization:
  li $sp, 0x10FFFFFC
  This is the largest address mapped to RAM

## Slide 11: Stack
Address | Contents
0x10FFFFF0 | 0x00000000
0x10FFFFF4 | 0x00000000
0x10FFFFF8 | 0x00000000
0x10FFFFFC | 0x00000000
$sp
li $sp, 0x10FFFFFC

## Slide 12: Stack
Address | Contents
0x10FFFFF0 | 0x00000000
0x10FFFFF4 | 0x00000000
0x10FFFFF8 | 0x00000000
0x10FFFFFC | 0x00000059
$sp
push $t1 # Assume $t1 has 0x59
$t1
Copied

## Slide 13: Stack
Address | Contents
0x10FFFFF0 | 0x00000000
0x10FFFFF4 | 0x00000000
0x10FFFFF8 | 0x00000059
0x10FFFFFC | 0x00000059
$sp
push $t1 # a second push
$t1
Copied

## Slide 14: Stack
Address | Contents
0x10FFFFF0 | 0x00000000
0x10FFFFF4 | 0x00000000
0x10FFFFF8 | 0x00000059
0x10FFFFFC | 0x00000059
$sp
pop $t2
$t2
Copied

## Slide 15: Stack
Address | Contents
0x10FFFFF0 | 0x00000000
0x10FFFFF4 | 0x00000000
0x10FFFFF8 | 0x00000059
0x10FFFFFC | 0x00000059
$sp
pop $t3 # a second pop
$t3
Copied

## Slide 16: Stack
Address | Contents
0x10FFFFF0 | 0x00000000
0x10FFFFF4 | 0x00000000
0x10FFFFF8 | 0x00000059
0x10FFFFFC | 0x00000059
$sp
Notice that even though things have been popped, they are still in memory

## Slide 17: PLPTool Memory Visulizer
Stack and other memory can be viewed with memory visualizer in simulation mode
  Simulation → Tools → Create a PLP CPU Memory Visualizer

## Slide 18: PLPTool Memory Visulizer

## Slide 19: Call
call label
  Saves current registers to stack
    Including return address
  Jumps to label
  NOTE: the stack pointer must be initialized in order to use call without receiving an error

## Slide 20: Return
return
  Restores registers from stack
  Jumps to the return address

## Slide 21: Call and Return Example

## Slide 22: PLP Datapath