## Slide 1: Branch and Jump Disassembly
Christopher Mar

## Slide 2: Jump Instruction Format
opcode
immediate value
6 bits
26 bits
PC = PC[31:28] + (imm << 2)
  RAM: 0x10000000 to 0x10FFFFFC
    First 4 bits of address always 0x1 (i.e. 0b0001)
  Word (4 byte) aligned memory means the lower 2 bits always 0’s, which is why we use a shift
    Save 2 bits in the immediate field

## Slide 3: Jump Instruction Format

## Slide 4: Calculate Jump Address
000010
00000000000000000000000110
6 bits
26 bits
PC = PC[31:28] + (imm << 2)
= 0x10000000 + (0b110 << 2)
= 0x10000000 + (0b11000)
= 0x10000000 + 0x18
= 0x10000018

## Slide 5: Branch Instruction Format
The value in rs and rt indicate which registers to compare
  5 bits can represent 32 numbers
  PLP has 32 registers
opcode
rs
6 bits
5 bits
rt
5 bits
offset
16 bits

## Slide 6: Branch Instruction Format
Offset is the signed value
  Number of instructions from the branch delay slot address to the label address
Offset is shifted left 2 bits (multiply by 4, size of a word) and added to the current PC value
opcode
rs
6 bits
5 bits
rt
5 bits
offset
16 bits

## Slide 7: Branch Offset

## Slide 8: Calculate Branch Offset
Offset: 0xFFFE is the signed value -2
  When branch is executed the PC is set to the current PC address plus -8 (-2 << 2 = -8)
Offsets can also be positive if the target label is after the current instruction
000101
01000
opcode
rs
00000
rt
1111 1111 1111 1110
offset

## Slide 9: Thanks for Watching