## Slide 1: Arrays and Sorting
Christopher Mar

## Slide 2: Array
Data structure
Array name is a pointer
  Memory address of first element
  Other elements accessed using offset (number of elements from first element)

## Slide 3: Array Data Access
Address | Contents
0x10000000 | 12
0x10000004 | 256
0x10000008 | 9
0x1000000C | 37
0x10000010 | 654
0x10000014 | 81
0x10000018 | 0
0x1000001C | 5309
register
lw
register
sw

## Slide 4: Traversing an Array
Loop that increments offset
my_array[i]
  Counter, i, is the offset from the base address

## Slide 5: Traversing an Array
Problem: in PLP offset is a fixed value
  Architectural choice limits lw/sw to 2 register accesses
Solution: save base address (if needed) and increment register pointing to array address

## Slide 6: Traversing an Array
Final Project:
  Values in array are 32-bit unsigned integers
  1 word (4 byte) offset per element

## Slide 7: Value Comparison (Inequality)
slt $rd, $rs, $rt
  If $rs < $rt then $rd set to 1 (true)
    Else $rd set to 0 (false)
  Result often used in a branch (compared with zero register)
    bne $rd, $0, was_less_than

## Slide 8: Inequalities
Inequality | Instruction | R if inequality is true
A < B | slt R, A, B | 1
A >= B | slt R, A, B | 0
A > B | slt R, B, A | 1
A <= B | slt R, B, A | 0

## Slide 9: PLPTool Memory Visulizer
Notes: Discussed in lecture 5

## Slide 10: PLPTool Memory Visulizer
Accessible while in simulation mode
  Simulation → Tools → Create a PLP CPU Memory Visualizer

## Slide 11: Thanks for Watching